Program:  TE CIVIL Engineering

Curriculum Scheme: Rev 2016

Examination: Third Year Semester V

Course Code: _____and Course Name: EE I    CBC

Time: 1 hour                                                                                           Max. Marks: 50

=====================================================================

All the Questions are compulsory and carry equal marks.

| Q1. | According to the Indian Standard recommendations, a water requirement of _______ per head per day is assumed for residential buildings. |
| --- | --- |
| Option A: | 50lit |
| Option B: | 115lit |
| Option C: | 135lit |
| Option D: | 160lit |
| Q2. | The diameter of main service pipe may vary from ___________ |
| Option A: | 2-15 mm |
| Option B: | 12-40 mm |
| Option C: | 50-75 mm |
| Option D: | 60-80 mm |
| Q3. | ___________ is used to measure flows to domestic buildings. |
| Option A: | Rain gauge |
| Option B: | Water tank |
| Option C: | Drainpipe |
| Option D: | Water meter |
| Q4. | The average quantity of water (in lpcd) required for domestic purposes according to IS code is ________ |
| Option A: | 100 |
| Option B: | 120 |
| Option C: | 70 |
| Option D: | 135 |
| Q5. | The average consumption of water required in factories in lpcd is ___________ a) 10-15 b) 20-30 c) 30-45 d) 70-80 |
| Option A: | 10-15 |
| Option B: | 20-30 |
| Option C: | 30-45 |
| Option D: | 70-80 |
| Q6. | The size of suspended solids lies in the range of ________ |
| Option A: | 10-3 – 10-6 mm |
| Option B: | 103 – 106 mm |
| Option C: | 10-1 – 10-3 mm |
| Option D: | 101 – 103 mm |
| Q7. | Which method is used to measure the color of water |
| Option A: | Gravimetric analysis |
| Option B: | Chromatography |
| Option C: | Tintometer method |
| Option D: | Hydrometer analysis |
| Q8. | Chlorides are estimated by titration with a standard silver nitrate solution by using _______ as an indicator. |
| Option A: | Potassium manganate |
| Option B: | Potassium chloride |
| Option C: | Potassium chromate |
| Option D: | Potassium dichromate |
| Q9. | One degree of hardness is equivalent to ___ ppm. |
| Option A: | 2 |
| Option B: | 1 |
| Option C: | 10 |
| Option D: | 100 |
| Q10. | ________ represents the bacterial density that is most likely to be present in water |
| Option A: | BOD |
| Option B: | COD |
| Option C: | MPN |
| Option D: | Coliform index |
| Q11. | The number of bacterial colonies by Agar plate count test should not exceed ____ per ml for potable water. |
| Option A: | 1 |
| Option B: | 10 |
| Option C: | 100 |
| Option D: | 1000 |
| Q12. | If the acid and gas are formed in the multiple tube fermentation technique, the test is _____ |
| Option A: | Positive |
| Option B: | Continued |
| Option C: | Negative |
| Option D: | Discarded |
| Q13. | How many types of aerators are commonly used in the treatment of water? |
| Option A: | 2 |
| Option B: | 3 |
| Option C: | 4 |
| Option D: | 5 |
| Q14. | Which process of water treatment is done to avoid floating debris, branches, trees or other large particles suspended in water? |
| Option A: | Screening |
| Option B: | Aeration |
| Option C: | Primary sedimentation |
| Option D: | Secondary sedimentation |
| Q15. | What is the size of the coarse screen used in pretreatment of water? |
| Option A: | 25mm |
| Option B: | 50mm |
| Option C: | 75mm |
| Option D: | 100mm |
| Q16. | __________ is an operation designed to force agitation in the fluid and induce coagulation. |
| Option A: | Sedimentation |
| Option B: | Flocculation |
| Option C: | Disinfection |
| Option D: | Aeration |
| Q17. | The depth of an enclosed tank of a rapid sand filter lies in the range of _____ |
| Option A: | 1-2m |
| Option B: | 2.5-3.5m |
| Option C: | 2-5m |
| Option D: | 3-5m |
| Q18. | When the pH is between 5 and 10, the chlorine in the water acts as _____ |
| Option A: | Hypochlorous acid |
| Option B: | Hypochlorite ions |
| Option C: | Molecular chlorine |
| Option D: | Hypochlorous acid hypochlorite ions |
| Q19. | Iron and Manganese are generally present in water supplies as ____________ |
| Option A: | Suspension |
| Option B: | Solution |
| Option C: | Colloidal particles |
| Option D: | Either suspension or solution |
| Q20. | By aeration process, dissolved iron is oxidized into ____________ |
| Option A: | Ferrous oxide |
| Option B: | Ferric oxide |
| Option C: | Ferrous hydroxide |
| Option D: | Ferric hydroxide |
| Q21. | Which gas is mainly produced due to incomplete burning of wood? |
| Option A: | CO |
| Option B: | SO2 |
| Option C: | NO2 |
| Option D: | NO3 |
| Q22. | What is the average concentration of ozone in the ozone layer of the atmosphere? |
| Option A: | Nearly 100% |
| Option B: | Greater than 90% |
| Option C: | Between 10-50% |
| Option D: | Less than 10ppm |
| Q23. | The ozone layer absorbs what range of wavelengths of the sun’s radiation? |
| Option A: | 0.80 nm – 1.50 nm |
| Option B: | 200 nm – 315 nm |
| Option C: | 450 nm – 570 nm |
| Option D: | 600 nm – 750 nm |
| Q24. | Which pollution cause hearing loss in organisms? |
| Option A: | Air pollution |
| Option B: | Noise pollution |
| Option C: | Water pollution |
| Option D: | Soil pollution |
| Q25. | At what decibel instantaneous rupture of membrane happens? |
| Option A: | 100 |
| Option B: | 120 |
| Option C: | 146 |
| Option D: | 150 |