Program:  TE CIVIL Engineering

Curriculum Scheme: Rev 2012

Examination: Third  Year Semester IV

Course Code: CE –C403 and Course Name: Structural Analysis I

Time: 1 hour                                                                                           Max. Marks: 50

=====================================================================

All the Questions are compulsory and carry equal marks .

| Q1. | What is the maximum shear force, when a cantilever beam is loaded with udl throughout? |
| --- | --- |
| Option A: | WxL |
| Option B: | W |
| Option C: | W/L |
| Option D: | W+L |
| Q2. | What will be the variation in BMD for the diagram? [Assume L = 2m]. |
| Option A: | Rectangular |
| Option B: | Trapezoidal |
| Option C: | Triangular |
| Option D: | Square |
| Q3. | What is the maximum bending moment for simply supported beam carrying a point load “W” kN at its centre? |
| Option A: | W kNm |
| Option B: | W/m kNm |
| Option C: | WxL kNm |
| Option D: | (WxL)/4 kNm |
| Q4. | ________ curve is formed due to bending of over hanging beams |
| Option A: | Elastic |
| Option B: | Plastic |
| Option C: | Flexural |
| Option D: | Axial |
| Q5. | What is the relation between work done by external loads and work done by internal loads. |
| Option A: | They are unequal |
| Option B: | They are equal |
| Option C: | Can’t say |
| Option D: | Depends upon load |
| Q6. | What is the shape of load-deformation curve for a linear elastic member? |
| Option A: | Straight line with constant slope |
| Option B: | Straight line with varying slope |
| Option C: | Curve |
| Option D: | Sine wave |
| Q7. | Conservation of energy will be applicable only when:- |
| Option A: | Static load is applied |
| Option B: | Dynamic load is applied |
| Option C: | Can be anything |
| Option D: | Large load is applied |
| Q8. | Fixed end moment due to support settlement is ---------. |
| Option A: | 96EIδ/L2 |
| Option B: | 6EIδ/L2 |
| Option C: | 6EIδ/L |
| Option D: | 4EIδ/L |
| Q9. | Fixed end moment for a fixed beam AB of span L loaded with central point load is W ------. |
| Option A: | WL/8 |
| Option B: | WL/10 |
| Option C: | WL/4 |
| Option D: | WL/2 |
| Q10. | A simply supported beam fixed at both ends can be analysis by ---------- |
| Option A: | Moment area method |
| Option B: | Conjugate beam method |
| Option C: | Three moment equation |
| Option D: | Work done |
| Q11. | If area of M/EI diagram between points A and B is –ve, then angle from tangent A to tangent B will be measured : |
| Option A: | Counterclockwise |
| Option B: | Clockwise |
| Option C: | Can be anything |
| Option D: | Can be anything zero |
| Q12. | The vertical deviation is measured along (if first point is A and second point is B):- |
| Option A: | A vertical line passing through centre of A and B |
| Option B: | A vertical line passing through A |
| Option C: | A vertical line passing through B |
| Option D: | A vertical line passing through either of the end points |
| Q13. | In general tA/B implies: |
| Option A: | Vertical deflection of tangent at B wrt that at A |
| Option B: | Vertical deflection of tangent at A wrt that at B |
| Option C: | Vertical deflection of extended tangent at B wrt tangent at A |
| Option D: | Vertical deflection of tangent at A wrt extended tangent at B |
| Q14 | P is treated here as:- |
| Option A: | Constant |
| Option B: | Variable |
| Option C: | it doesn’t matter |
| Option D: | depends upon load |
| Q15. | What will be the work done if all three forces are place at once on the beam? |
| Option A: | (p1 + dp1)(Δ1 + dΔ1) + (p2)( Δ2 + dΔ2) |
| Option B: | (p1 + dp1)(Δ1 + dΔ1) + 1⁄2 (p2)( Δ2 + dΔ2) |
| Option C: | 1⁄2 (p1 + dp1)(Δ1 + dΔ1) + (p2)( Δ2 + dΔ2) |
| Option D: | 1⁄2 (p1 + dp1)(Δ1 + dΔ1) + 1⁄2 (p2)( Δ2 + dΔ2) |
| Q16. | What is change in length of member if temperature increases by ΔT and expansion coefficient is ά? |
| Option A: | 1⁄4 ά ΔTL |
| Option B: | 1⁄3 ά ΔTL |
| Option C: | 1⁄2 ά ΔTL |
| Option D: | ά ΔTL |
| Q17. | If any of the external forces acting increases, then internal energy would:- |
| Option A: | Decrease |
| Option B: | Increase |
| Option C: | Not change |
| Option D: | Become –ve |
| Q18. | For drawing ILD, what value of test load is assumed? |
| Option A: | 1 unit |
| Option B: | Arbitrary |
| Option C: | Depends upon structure |
| Option D: | 0 |
| Q19. | Top most part of an arch is called ________ |
| Option A: | Sofit |
| Option B: | Crown |
| Option C: | Center |
| Option D: | Abutment |
| Q20. | Shape of three hinged arch is always :- |
| Option A: | Hyperbolic |
| Option B: | Circular |
| Option C: | Parabolic |
| Option D: | Can be any arbitrary curve |
| Q21. | In force analysis, weight of cable is generally ________ |
| Option A: | Added |
| Option B: | Neglected |
| Option C: | Added in some, neglected in others arbitrarily |
| Option D: | Depends upon magnitude of other load |
| Q22. | It is generally assumed that the cable is _________ |
| Option A: | Perfectly flexible |
| Option B: | Perfectly inflexible |
| Option C: | Inextensible |
| Option D: | Perfectly flexible and extensible |
| Q23. | __________ is a vertical member subjected to direct compressive force. |
| Option A: | Strut |
| Option B: | Beam |
| Option C: | Column |
| Option D: | Post |
| Q24. | A body having similar properties throughout its volume is said to be _____________ |
| Option A: | Isotropic |
| Option B: | Homogeneous |
| Option C: | Continuous |
| Option D: | Uniform |
| Q25. | Materials exhibiting time bound behaviour are known as ______ |
| Option A: | Isentropic |
| Option B: | Reactive |
| Option C: | Fissile |
| Option D: | Visco elastic |